## Slide 1: Peering at the Internet’s Frontier: A First Look at ISP Interconnectivity in Africa
Arpit Gupta Georgia Tech
Matt Calder (USC), Nick Feamster (Georgia Tech), Marshini Chetty (Maryland), Enrico Calandro (Research ICT Africa), Ethan Katz-Bassett (USC)
Notes: I will talk about my paper on “”
Joint effort of researchers in Georgia Tech, Maryland, Research ICT Africa and USC
In this talk I will see why we observe degraded Internet performance in Africa and how we can solve these problems

## Slide 2
Broadband Connectivity in Africa
According to ITU in 2013
93 million broadband subscriptions
27% growth in past 4 years (Highest)
Broadband associated with economic growth + development
Yet, very little is known about performance in Africa and what causes poor performance when it does arise.
Notes: End with slide like:
So question to ask here is how well does broadband performs in Africa

## Slide 3
How Well Does Broadband Perform?

## Slide 4: Latencies to Nearby Locations are High
Latencies from South Africa to Kenya, Brazil, India are 2x higher than latencies to Europe.
Kenya
Brazil
India
Europe
Latencies (ms)
100
300
500
Notes: In our previous works we identified that latencies to nearby locations are high

## Slide 5: Latencies are Even Higher During Failures
March 27, 2013 0620 UTC: SWM4 Fiber Cut
All BISmark hosts could not reach KENet for 3+ hours
Latencies remain high for another 8+ hours (except for Neotel, in South Africa)
Latencies remain high from Europe and North America. Only one AS in S. Africa, Neotel sees decent latency after 3 hours.
More details: http://connectionmanagement.org
Notes: Even under normal conditions latencies to nearby locations like Kenya is significantly high. What can be the reason for such a high latency

## Slide 6: Causes of High Latency: Circuitous Routing Paths
Europe/ US
Africa
South Africa
LINX (London
Kenya
9000 km
3000 km
7000 km
Notes: Given this context we tried to answer two important questions

## Slide 7: Two Questions
What is the nature of Internet interconnectivity (between ISPs) in Africa?
What can be done to reduce latency to common Internet services?

## Slide 8: Two Questions
What is the nature of Internet interconnectivity (between ISPs) in Africa?
What can be done to reduce latency to common Internet services?

## Slide 9: BISmark: Measurements from Fixed Locations
Users install routers in home networks
Custom firmware performs periodic measurements
Can aggregate by country, city, ISP
Example: Cape Town Users
175+ Active Routers, 20+ countries
Notes: Emulates Internet performance observed by end users or eyeballs

## Slide 10: BISmark Deployment in South Africa
Periodic latency and throughput measurements
Traceroutes to explain the cause of path performance
Router-based deployment
  17 home networks, 7 ISPs, all 9 provinces

## Slide 11: Destinations for Traceroute Probes
Global M-Lab Servers
Google Caches in Africa

## Slide 12: High Latencies to Nearby Locations…
…
7, 196.44.0.74, 7.793, South Africa, AS16637
8, 196.223.22.24, 8.338, South Africa, Cape Town IXP
9, 41.164.0.243, 34.679, South Africa, AS36937
…
14, 196.24.45.146, 92.511, South Africa, AS2018
…
8, 209.212.111.201, 199.446, South Africa, AS16637
9, 195.66.225.31, 217.301, United Kingdom, London IXP (LINX)
10, 196.32.209.77, 201.569, South Africa, AS36944
…
14, 197.136.0.108, 368.107, Kenya, AS36914
High Latency
Cape Town (SA) to M-Lab Johannesburg (SA)
Cape Town (SA) to M-Lab Nairobi (KE)
Notes: The circuitous routing paths are indicators of poor ISP interconnectivity in Africa

## Slide 13: … Circuitous Routing Paths
…
7, 196.44.0.74, 7.793, South Africa, AS16637
8, 196.223.22.24, 8.338, South Africa, Cape Town IXP
9, 41.164.0.243, 34.679, South Africa, AS36937
…
14, 196.24.45.146, 92.511, South Africa, AS2018
…
8, 209.212.111.201, 199.446, South Africa, AS16637
9, 195.66.225.31, 217.301, United Kingdom, London IXP (LINX)
10, 196.32.209.77, 201.569, Kenya, AS36944
…
14, 197.136.0.108, 368.107, Kenya, AS36914
Cape Town (SA) to M-Lab Johannesburg (SA)
Cape Town (SA) to M-Lab Nairobi (KE)
Packets leaving Africa

## Slide 14: Poor ISP Interconnectivity in Africa
Reasons
    Local ISPs not present at regional IXPs
    IXP participants don’t peer with each other
Consequences
  Local traffic does not stay local
  Paths leave continent

## Slide 15: Local ISPs not Present at Regional IXPs
ISPs prioritize connecting to European IXPs
Lesser incentives to connect at regional ones
South Africa
Kenya
JINX
(Johannesburg)
KIXP (Nairobi)
Liquid Telecom
KENET
Notes: Like one stop shop for these local ISPs

## Slide 16: Missing Peering Links at Regional IXPs
Most content not available locally
Less incentive to peer with local ISPs
South Africa
Kenya
JINX (Johannesburg)
KIXP (Nairobi)
MTN, SA
MTN, KE
IS, SA
IS, KE
KENET

## Slide 17: Regional IXPs Only Prevalent on Intra-Country Paths
Between South Africa and Kenya: Few Paths have Regional IXPs
M-Lab Nairobi
Within South Africa: High Fraction of Paths Have at Least one Major Regional IXP
M-Lab Johannesburg
BISmark Routers (Fraction)
BISmark Routers (Fraction)
IXP Prevalence (Normalized)
JINX (SA) is most prevalent
LINX (UK) is most prevalent
IXP Prevalence (Normalized)

## Slide 18: Two Questions
What is the nature of Internet interconnectivity (between ISPs) in Africa?
What can be done to reduce latency to common Internet services?

## Slide 19: Solution #1: Add More Caches
Traceroute Probes between BISmark routers (eyeball) and Google Cache Node in Uganda (content)
Google cache hosted by MTN
Emulates scenario where content is in nearby country
BISmark Routers
Inside Customer Cone
Latency Improvements
Latency improvements are limited when peering to the cache is not adequate.

## Slide 20: Solution #2: Add More Peering Links
Simulation: Add peering links between all the participants at
  JINX (Johannesburg)
  KIXP (Nairobi)
Emulates scenario where more ISPs connect and peer at regional IXPs
Latency Improvements
Δ ~ 250ms
Additional peering links  Significant latency improvements
Notes: Adding cache nodes improves latency performance and adding more peering links ensures that this benefit trickles down to more number of users

## Slide 21: Better Peering is a Substitute for Additional Caches
Experiment:
  add caches in Kenya
  traceroute Probe from SA
Two scenarios
  Use existing peering links
  Add more peering links
Additional caches have little effect on average latency (compared to adding more peering links).
Additional Links
Existing Links

## Slide 22: Summary
What is the nature of Internet interconnectivity (between ISPs) in Africa?
  Many ISPs are not present in regional IXPs
  Many ISPs do not interconnect at regional IXPs
What can be done to reduce latency to common Internet services?
  Peering at regional IXPs can reduce median intra-continent latencies by 250ms
Next steps: Better incentives for interconnectivity
Arpit Gupta
agupta80@gatech.edu

## Slide 23: Backup Slides

## Slide 24: High Latency Paths within Africa
24
M-Lab Servers
Normalized Latency:
  Ratio of observed and speed of light propagation latencies
  Darker blocks imply higher latency penalties
High Penalties for routes to M-Lab server in Nairobi
Geographical Distance
High Normalized Latency

## Slide 25: IXP Prevalence
Quantifies presence of IXPs for routing paths
Similar to routing path prevalence
Lower IXP prevalence observed for circuitous routing paths